## Slide 1: The influence of Low Impact Development on rainfall-runoff relationships at catchment scale
Xinxin Sui
MSc Water Management 2017-2019
TU Delft

## Slide 2: The influence of Low Impact Development on rainfall-runoff relationships at catchment scale
Introduction
Modelling
Scenarios
Results
Discussions
Conclusions
Recommendations

## Slide 3: Introduction
Low Impact Development
Problem statement
Research approach
Study area
Data
Conventional development (CD: disturbance of nature)
urban water problems
Low Impact Development (mimic nature)
solve water problems
Notes: LID, solve problem by TD; disturbance; concrete, asphalt, remove soil, cut trees, (dry/flood), water quality; LID Green, Blue e.g. green roof, pervious pavement; decrease impact of urban construction, at a stable level

## Slide 4
LID seems to decrease runoff
Flood risk: Delayed function of LID The approaching of urban and rural peak times  more stacking of urban and rural peaks and larger total peak
Trend of Urbanization
Low Impact Development
Problem statement
Research approach
Study area
Data
Chart: 
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90
Rural Areas | 0.1 | 0.1 | 0.11 | 0.13 | 0.15 | 0.17 | 0.2 | 0.24 | 0.3 | 0.36 | 0.41 | 0.44 | 0.45 | 0.42 | 0.35 | 0.27 | 0.2 | 0.14 | 0.1
CD Urban Areas | 0.1 | 0.18 | 0.28 | 0.4 | 0.55 | 0.75 | 0.88 | 0.9 | 0.83 | 0.69 | 0.5 | 0.38 | 0.3 | 0.23 | 0.17 | 0.12 | 0.105 | 0.1 | 0.1
LID Urban Areas | 0.1 | 0.1 | 0.135 | 0.18 | 0.24 | 0.32 | 0.4 | 0.49 | 0.6 | 0.72 | 0.75 | 0.7 | 0.58 | 0.47 | 0.38 | 0.3 | 0.22 | 0.15 | 0.1
CD catchment | 0.2 | 0.28 | 0.39 | 0.53 | 0.7 | 0.92 | 1.08 | 1.14 | 1.13 | 1.05 | 0.91 | 0.82 | 0.75 | 0.65 | 0.52 | 0.39 | 0.305 | 0.24 | 0.2
LID catchment | 0.2 | 0.2 | 0.245 | 0.31 | 0.39 | 0.49 | 0.6 | 0.73 | 0.9 | 1.08 | 1.16 | 1.14 | 1.03 | 0.89 | 0.73 | 0.57 | 0.42 | 0.29 | 0.2
Introduction
Notes: Delayed function of LID, peak times approach, which cause more stacking

## Slide 5
Low Impact Development
Problem statement
Research approach
Study area
Data
Main Q: Explore the impact of LID implementation with regard to peak runoff value on the catchment scale
Q1: The different hydrologic characters of urban and rural areas;
Q2: The urbanization influence on rainfall-runoff relationship on catchment scale;
Q3: The LID implementation influence on rainfall-runoff relationship on catchment scale;
Q4: The problem caused by the time approaching and stacking of peak flows from urban and rural areas due to LID;
To deal with the prediction uncertainty, scenario analysis is used to give a reliable answer to the research question.
Introduction

## Slide 6
This project will exploit conceptual hydrological model with SUPERFLEX model framework to simulate one real catchment under three different conditions.
Current CD situation
Urbanized CD situation under 3 urbanization scenarios (without LID practices)
Urbanized LID situation under 5 LID implementation scenarios
Introduction
Low Impact Development
Problem statement
Research approach
Study area
Data

## Slide 7
Location: San Antonio city in Texas state, U.S. (29.424349; -98.491142)
Area: 4544 km2 (Rural, 73%; Urban 27%)
Condition: The position of urban areas
Low Impact Development
Problem statement
Research approach
Study area
Data
Introduction

## Slide 8
Social condition: the seventh most populous city in the U.S. with 1.5 million residents (2017)
Climate: transitional humid subtropical climate (Winters may pass without any frozen precipitation at all)
Geology: moderately permeable deep clayey soils and marls
Urban water system: separate sewer and stormwater systems
Low Impact Development
Problem statement
Research approach
Study area
Data
Introduction
Chart: Year
| 2017 | 2016 | 2015 | 2014 | 2013 | 2012 | 2011 | 2010
Annual Growth Rate | 0.0163 | 0.0161 | 0.0199 | 0.0189 | 0.0184 | 0.0189 | 0.0184 | 0.0154

## Slide 9
Geohydrology: prolific Edwards Aquifer provides the urban usage water for San Antonio City; recharge project in contribution zone (in north part of San Antonio City)
Low Impact Development
Problem statement
Research approach
Study area
Data
Introduction
Figure. The distribution area of Edwards Aquifer and the location of San Antonio City (Resources: Wikipedia)

## Slide 10
Low Impact Development
Problem statement
Research approach
Study area
Data
Introduction
Type: Precipitation; Discharge; Evaporation
Available period: 2017-04-12 to 2018-12-02 (600 days)
Time scale: 30 minutes (The number of data = 28800)
Resources: USGS website

## Slide 11: The influence of Low Impact Development on rainfall-runoff relationships at catchment scale
Introduction
Methodology
Modelling
Scenarios
Results
Discussions
Conclusions and recommendations

## Slide 12: Methodology
Conceptual versus physical-based model: to reduce the equifinality and model uncertainty problems; low data requirement
Semi-distributed versus distributed model: more simple model, to reduce the equifinality and model uncertainty problems
Flexible framework versus fixed model structure: identify the dominant hydrological process and understand the hydrological condition by hypothesizing, building, and testing different model structures; tailor-made model can fit the condition of study catchment as much as possible.
Final selection: SUPERFLEX framework
Rainfall-runoff model selection
Modelling Strategy
The expression of LID in model

## Slide 13: Methodology
Strategy of model structure design: start from two lumped models
Parameter calibration method:
Period: all 600 days for two sub-catchments and the first 365 days of study catchment;
Objective function: Nash Sutcliffe Efficiency (NSE) and correlation coefficient (R2);
Creating parameter set: Monte Carlo method; More complex models with more parameters will have more set of parameter samples to seek a “fair” calibration scale
For the semi-distributed models, some constraints on the rural and urban parameters will be exploited to avoid unrealistic combinations of parameters
(Rainfall-runoff model selection)
Modelling Strategy
The expression of LID in model

## Slide 14: Methodology
3. Model components or model selection strategy
For lumped models:
dominant water process;
effective and efficient components;
For semi-distributed models:
accuracy and precision (selecting model structure)
performance of rural and urban sub-flows and peak flow simulation (selecting parameter set)
distribution comparison (QQ plot) of observed data and model result (selecting parameter set)
(Rainfall-runoff model selection)
Modelling Strategy
The expression of LID in model

## Slide 15: Methodology
(Rainfall-runoff model selection)
Modelling Strategy
The expression of LID in model
Qualitative hydrologic routes design: hydrologic functions, e.g. infiltration or transpiration;
Quantitative parameters estimation: relevant literature, realistic field test results, and local government files of LID practices.

## Slide 16: The influence of Low Impact Development on rainfall-runoff relationships at catchment scale
Introduction
Modelling
Scenarios
Results
Discussions
Conclusions
Recommendations

## Slide 17: Modelling
M01 |  | 
 |  | M04
M02 |  | 
 |  | M05
M03 |  | 
a. Urban lumped model development (for urban sub-catchment)
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
Slow groundwater Reservoir
Fast groundwater Reservoir
Human impact Reservoir
Interception Reservoir
Notes: Bucket as basic model framework is tested among different model generations; among the several models in one generation, different hydrological processes and constitutive functions are tested

## Slide 18: Modelling
M04A |  | M04C
M04B |  | 
 |  | M04D
a. Urban lumped model development (M04 as example)
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
D:
precipitation distribution coefficient
Alpha:
discharge coefficient
Cr:
Capillary rise
Notes: Bucket as basic model framework is tested among different model generations; among the several models in one generation, different hydrological processes and constitutive functions are tested

## Slide 19: Modelling
b. Urban lumped model result
Figure 12. Model Result of Urban Lumped M05B
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model

## Slide 20: Modelling
c. Model components selection: dominant; effective and efficient
By comparing 5 generations of model structure:
“Unsaturated Reservoir-Slow groundwater Reservoir-Human impact Reservoir” three buckets as basic model framework;
Although Interception Reservoir does not have positive effect on the NSE, the model performance on peak runoff simulation is improved.
By comparing different model structures of one generation:
Capillary rise (Cr);
Discharge exponent (α);
Precipitation distribution factor (D);
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model

## Slide 21: Modelling
d. Parameter calibration of lumped model
- Determine initial parameter intervals in semi-distributed model
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
parameter intervals, rather than specific parameter value;
Notes: No specific parameter value would be selected from this calibration result but the parameter intervals, which could capture the objective function larger than 0.6, were reserved and used to determine the initial parameter interval in semi-distributed model

## Slide 22: Modelling
d. Parameter calibration of lumped model
- Determine initial parameter intervals in semi-distributed model
Figure 109. Parameter Calibration Result of Urban Lumped M05B (The parameter intervals, which could capture the objective function larger than 0.6, were reserved and used to determine the initial parameter interval in semi-distributed model.)
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
parameter intervals, rather than specific parameter value;
Realistic range;
capture the objective function larger than 0.6
Notes: No specific parameter value would be selected from this calibration result but the parameter intervals, which could capture the objective function larger than 0.6, were reserved and used to determine the initial parameter interval in semi-distributed model

## Slide 23: Modelling
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
Precipitation distribution factor (D): construction degree
Discharge coefficient of HR (Kh): water conveyance efficiency
Recharge coefficient (Rc): uneven groundwater recharge
Discharge coefficient of SR (Ks): groundwater stock in SR
e. The hydrological difference between urban sub-catchment
and study catchment (Human activities vary a lot by region)
- Determine initial parameter intervals in semi-distributed model
Notes: The calibration intervals of some para in semi should be changed.

## Slide 24: Modelling
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
a. Key elements in semi-distributed model
Time lag for rural area, since the position of rural area (Initial interval: 1.25 - 10 hours)
Human activity module for urban area
Constraints on parameter limitation

## Slide 25: Modelling
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
a. Key elements in semi-distributed model
Time lag for rural area (Initial interval: 1.25 - 10 hours)
Human activity module for urban grey areas (impervious areas)
Constraints on parameter limitation
Figure 17. Schematic figure of designed Human Impact Module
Figure 16. The calibration result of water pumping process
Precipitation on
urban grey areas
Precipitation on
urban green areas
Discharge from urban pipeline system
Groundwater
recharge
Groundwater
pumping
Notes: HR: human impact reservior

## Slide 26: Modelling
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
a. Key elements in semi-distributed model
Time lag for rural area (Initial interval: 1.25 - 10 hours)
Human activity module for urban area
Constraints to avoid unrealistic combination of parameters
1. Pmax,R > Pmax,U (The maximum percolation velocity)
2. Sumax,R > Sumax,U (The maximum unsaturated storage depth)

## Slide 27
M01A |  | M03A
(6R) |  | (7R)
M01B |  | M03B
M02 |  | M04
(7R) |  | (8R)
Riparian
Reservoir
Interception
Reservoir
Interception
Reservoir
RR & IR
Notes: b. Model structure generation of Semi-distributed model

## Slide 28
M01A |  | M03A
M01B |  | M03B
M02 |  | M04
D-Prec. Dist. coefficient
D-Prec. Dist. coefficient
Notes: b. Model structure generation of Semi-distributed model

## Slide 29: Modelling
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
c. Selection of Semi-distributed model
The selection of model structure
The determination of propriate parameter set

## Slide 30: Modelling
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
c. Selection of Semi-distributed model
The selection of model structure
The determination of propriate parameter set:
1. The performance on sub-flows and basin peak runoff
2. Distribution analysis (QQ plots)

## Slide 31: Modelling
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
d. The final selection of rainfall-runoff semi-distributed model for current condition

## Slide 32: Modelling
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
d. The final selection of rainfall-runoff semi-distributed model for current condition

## Slide 33: Modelling
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
a. Qualitative hydrologic routes of four representative LID practices
(Bioretention cells as example)
Interception
transpiration
infiltration
storage
delay
Symbols: ++ major function; + accessory function; - insignificant function;

## Slide 34: Modelling
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
b. Quantitative parameters estimation
1. Precipitation distribution factor (DLID);
2. The ratio of drainage area to construction area (AR);
3. The maximum interception depth (Imax,B): 3.5 mm
- 0.6 to 4.6 mm, field tests in Maryland, U.S. (Li et al , 2009);
4. The maximum water storage depth in soil layer (Sumax): 300 mm
- “SARA LID Guidance Manual” recommends 0.6 - 1.2 m soil media depth;
- Empirical soil porosity as 0.35 for moderately permeable local soil;
5. Time lag coefficient of bioretention cells (TlagB): 3h
-according to a field test result, peak flow could be delayed by 3 hours by bioretention cells (Hunt., 2008);

## Slide 35: Modelling
Lumped models for rural and urban sub-catchments
Semi-distributed model for study catchment
The expression of LID practices in model
 | Vegetated Swales
Pervious pavements | 
 | Green Roofs
Notes: With the same procedures, the modules for the another three representative LID practices are designed

## Slide 36: Modelling
The expression of LID practices in model: the parameter estimation results of four LID practices

## Slide 37: The influence of Low Impact Development on rainfall-runoff relationships at catchment scale
Introduction
Modelling
Scenarios
Results
Discussions
Conclusions
Recommendations

## Slide 38: Scenarios
Urban development scenarios
LID implementation scenarios
Population Forecast: 2.4 million in 2040
Urban development strategy: Higher density, less expansion; since the former unconstrained outward urban expansion has led to disinvestment in the urban core areas and high cost of infrastructure and utility service
a. Scenarios design of urban development
Notes: 3 urban development scenarios are designed according to different urban expansion extent

## Slide 39: Scenarios
Urban development scenarios
LID implementation scenarios
b. The expression of urban development scenarios in model
The distribution of rural and urban areas;
The distribution of urban green and grey areas (D);
Two assumptions:
Uniform construction degree;
More infill urban development, less per capita urban grey areas: 3 estimate ratios for the compaction degree of living space (0.85, 0.9, 1)
Notes: Larger population density, the

## Slide 40: Scenarios
Urban development scenarios
LID implementation scenarios
Five scenarios are formulated and tested based on the urban development scenario C (half infill and half sprawl strategy).
Bioretention: 15% (precipitation on urban grey areas);
Vegetated Swales: 15%;
Green roofs: 15%;
Pervious pavement: 15%;
Mixed LID scenario: Bioretention cells 15% (AR = 1.5); Vegetated swales 15% (AR = 3); green roofs 5%; permeable pavements 15%; Cascade connection among LID practices;
AR: the ratio of drainage areas and construction areas
Notes: The first four LID scenarios are aim to compare the different hydrologic performances of LID practices; the ratio of drainage areas and construction areas

## Slide 41: The influence of Low Impact Development on rainfall-runoff relationships at catchment scale
Introduction
Modelling
Scenarios
Results
Discussions
Conclusions
Recommendations

## Slide 42: Results
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
 | Evaporation | Water storage | Runoff delay
Rural | + | + | +
Urban | - | - | -
a. The parameters calibration result of rural and urban lumped models
Evaporation
correction
coefficient
Maximum
unsaturated
storage
Slow groundwater
flow
coefficient
Time lag
coefficient
Groundwater flow
+
-
Symbols: + strong; - weak;
Notes: Most of the four parameters for urban areas are smaller than them for rural areas; and these four parameters quantified the E/S/D/GF ability. Therefore with less E/S/D, urban peak larger than rural peak; With less gw recharge, the urban base flow will less than rural base flow.

## Slide 43: Results
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
In general, the runoff from rural areas performs more moderate than it from urban areas.
Urban: varies between extreme flood and extreme drought;
Rural: the peak flows seldom happen in dry seasons, but in flood season, the magnitude of peaks may be great.
(And the presence of peak runoff is always accompanied with the increase of base flow caused by large groundwater stock.)
b. The comparison of rainfall-runoff relationship of urban and rural areas

## Slide 44: Results
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
Figure 32. The total basin runoffs of the three urban developed scenarios
The maximum peak runoff

## Slide 45: Results
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
Figure 34. The water input and output of urban drainage system (HR) in current situation and urban development scenario A
The decrease of extreme peak flow in Scenario A
Scenario A: has larger urban grey areas and less urban green areas
Small to medium peaks: only generate from urban grey areas, increase;
Extreme large peaks in flood season: mainly generate from large area of urban green surface (and rural areas), decrease;
Notes: abnormal phenomenon could be explained by the generation mechanism of peak runoffs; this argument can be proved with this figure; And the output of HR is the main resource of urban runoff. therefore with A, the first vertex increased but the second larger peak decrease.

## Slide 46: Results
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
Figure 35. The total basin runoff of five LID scenarios and the CD scenario
a. Less effective on basin peak runoff reduction in flood season
Reason 1. LID practices influence urban grey areas; however peaks in flood season are generated from rural and urban green areas.
Reason 2. Intensive rainfalls take up most space of LID practices and exhaust the water retention capacity.
Notes: Several characteristics of LID performance are founded here

## Slide 47: Results
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
Figure 35. The total basin runoff of five LID scenarios and the CD scenario
b. LID practices have more significant effect on the first vertex
The first peak vertex mainly generates from urban grey areas;
The second vertex mainly generates from large areas of urban green surface or rural areas, which are not the “domain” of LID.
Typical extreme peak

## Slide 48: Results
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
c. The comparison of 4 LID practices
(the first 4 scenarios with single LID practices)
Bioretention cells, pervious pavements: forceful runoff volume and peak runoff reduction ability;
Vegetated Swales: weak runoff volume reduction ability;
Green Roofs: weak peak runoff reduction ability, lose function in flood seasons, since small water retention capacity.

## Slide 49: Results
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
d. More water input and less construction areas for bioretention cells
(Mixed scenario & Bioretention scenario)
The ratio of overflow kept the same
Infiltration decreases: less construction areas ;
Evaporation (Interception and transpiration): better developed.
Great runoff reduction potential, especially evaporation;
Table 54. Performance comparison of bioretention cells in mixed LID scenario and single bioretention scenario
 | Drainage area (of urban grey area) | Construction area (of urban grey area) | Water input (mm)
Mixed scenario | 15% | 10% | 497
Bioretention scenario | 15% | 15% | 437
Notes: The hydrological performance of bio could further explored by comparing bio scenario and mixed LID scenario. In mixed,

## Slide 50: Results
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
e. Mixed LID scenario (based on urban development scenario C)
Most peaks (generating from urban grey areas) are controlled well.
Extreme large peaks in flood season (also generating from rural and urban green areas): the peak reduction ability was restrained significantly; But larger extent of infill urban development strategy (like scenario A) could be used to solve this problem;
Table 55. Model results of the total basin runoff in mixed LID scenario, the current CD scenario and the CD scenario in 2040

## Slide 51: Results
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
a. Four scenarios with single LID practice
Time lags between LID and CD urban peaks: 0.5 - 2.5 hours;
(Time lags between rural peaks and CD urban peaks: 6.5 - 15.5 hours;)
delay ability < reduction ability, most basin peak runoffs decrease
Table 55. Model results of the total basin runoff in mixed LID scenario, the current CD scenario and the CD scenario in 2040

## Slide 52: Results
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
b. The mixed LID practices scenario
Time lags between LID and CD urban peaks: 0.5 - 6.5 hours;
(Dry season: reduction ability > delay ability, basin peaks decrease)
Flood season: reduction ability < delay ability, basin peaks increase
Urban runoff (L): increased by 0.06 mm/d, from 1.62 to 1.68 mm/d;
Total basin runoff (L): increased by 0.08 mm/d, from 3.57 to 3.65 mm/d;
Total basin runoff (R): increased by 0.12 mm/d, from 6.35 to 6.47 mm/d.
Figure 40. The peak runoffs from rural, urban, and basin areas in mixed LID practices scenario and CD scenario
Notes: . In conclusion we may say that the stacking effect of LID implementation on total basin runoff is limited in the case of San Antonio basin, partly due to the fact that only a small part of this basin is urbanized.

## Slide 53: The influence of Low Impact Development on rainfall-runoff relationships at catchment scale
Introduction
Modelling
Scenarios
Results
Discussions
Conclusions
Recommendations

## Slide 54: Discussions
Model uncertainty
Scenario limitation
The comparability of research results and literatures about LID
a. Low complexity of model structure
Overlook the heterogeneity within the rural or urban areas;
Reliability and accuracy of the mathematical expressions of many artificial water processes (such as urban stormwater drainage, water pumping, and groundwater recharge) are arguable;
b. The model components inheritance from lumped to semi-distributed model
Some information may be lost;
c. Optimistic LID parameters estimation
Optimistic estimation of LID practices condition (such as 12-cm soil depth for extensive green roofs)
The negative events, such as the damage of LID practices, lack of daily maintenance or blockage problems of soil media, are neglected .

## Slide 55: Discussions
Model uncertainty
Scenario limitation
The comparability of research results and literatures about LID
a. The limitation of urban development scenarios
Population forecast: 0.9 million new residents between 2017 and 2040;
Uniform construction degree;
3 estimate ratios for the compaction degree of living space (0.85, 0.9, 1).
b. The limitation of LID implementation scenarios
Uniform LID implementation;
Optimistic design: 50% of the precipitation on urban impervious surface is collected, and cascade connections for mixed LID scenarios.
Notes: Scenario limitations are mainly comes from the reliability of the forecast and assumption such as the population forecast and the assumption of uniform construction degree.

## Slide 56: Discussions
Model uncertainty
Scenario limitation
The comparability of research results and literatures about LID
a. The comparability of model result
b. Analysis comparability
Ineffective runoff reduction performance (total volume) of vegetated swales is ascribed to its fast rainwater transportation and short residence time (Huang, 2018).
Permeable pavement is the most hydrologically effective LID practice among the four test LID practices (Ahiablame, 2012).
Compared to single LID practices, the mixed of various LID practices should be promoted with better robustness (Qin, 2013; Askarizadeh, 2015; Fang, 2017; Huang, 2018).
The reduction of total runoff volume | Literatures (Resources) | This research
Bioretention cells | 48% - 97% (Chapman and Horner, 2010; DeBusk and Wynn, 2011) | 84%
Green roofs | 23% - 100% (VanWoert, 2005; Hathaway, 2008; Carpenter and Kaluvakolanu, 2011) | 63%
Permeable pavements | 50% - 93% (Rushton, 2001; Hunt, 2002; Dreelin, 2006) | 91%
Vegetated swales | 85% for small storms; 35% - 66% for large storms (Hunt, 2010) | 25% for all the storms in total
Notes: Most of the results are consistent with literatures. And for the result analysis, this research provides some similar arguments as literatures; such as

## Slide 57: The influence of Low Impact Development on rainfall-runoff relationships at catchment scale
Introduction
Modelling
Scenarios
Results
Discussions
Conclusions
Recommendations

## Slide 58: Conclusions
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
Since the specific conditions of study catchment, some quantitative conclusions of this research are limited in a restrained region.
Q1 :
Urban: varies between extreme flood and extreme drought;
Rural: more moderate, but in flood season peak runoffs may be large.
Q2 :
The infill urban development strategy is more helpful on runoff reduction than sprawl urban development strategy.
For the scenario C (half-infill and half-sprawl), the total runoff volume would rise by 14% compared to current situation. And for scenarios B (70%-infill and 30%-sprawl), the total runoff would rise by 9% in. As for scenario A (full infill development), this growth rate is only 3%.
For scenario C and scenario B, the peak runoff of a typical extreme peak increased by 16% and 8% than current situation, however scenario A even decreased the peak runoff by 4%.

## Slide 59: Conclusions
Q1: The different rainfall-runoff relationship of urban and rural areas
Q2: Urbanization influences
Q3: LID implementation influences
Q4: The time approaching and stacking of urban and rural peaks due to LID implementation
Q3 :
LID practices are less effective on peak runoff reduction in flood season than dry season;
Bioretention cells and pervious pavements have forceful runoff reduction ability; The runoff volume reduction ability of vegetated swales is weak; Green Roofs performed worst on peak runoff reduction;
More water input and less construction areas could better develop the evaporation ability of bioretention cells;
Q4:
For four scenarios with single LID practice (15%), the peak delay is not significant, and therefore there is no obvious increase on basin peaks.
For the mixed LID scenarios (50%), the delayed urban runoff brings larger stack of rural and urban peaks and increases two basin peak runoffs in flood season from 3.57 to 3.65 mm/d and from 6.35 to 6.47 mm/d.

## Slide 60: The influence of Low Impact Development on rainfall-runoff relationships at catchment scale
Introduction
Modelling
Scenarios
Results
Discussions
Conclusions
Recommendations

## Slide 61: recommendations
Recommendations for the suitable LID implementation
Recommendations and suggestions for future research
The combination of various LID practices rather than single LID; and cascade connections among different LID practices
The infill development strategy is more helpful on runoff reduction than sprawl development strategy,
When making urban development and LID implementation plans, the time difference between the peak runoffs from the sub-areas (rural areas, urban grey and green areas; bare, grass, bush and tree areas) could be design by adjusting the area and position of sub-areas. Therefore, the basin peak runoffs could be controlled.
Future research could exploit distributed models to further explore the influence of heterogeneous urban condition (caused by urban drainage system, regional water police, partial construction degree and etc).
Notes: Cascade connection, to better balance the different water retention capacity of LID practices.

## Slide 62: The influence of Low Impact Development on rainfall-runoff relationships at catchment scale Thank you for your listening!
Xinxin Sui
MSc Water Management 2017-2019
TU Delft